## Slide 1
Colpex
The Cold Pooling Experiment
Prof. Peter Clark
Mathematics / CCE

## Slide 2: Peter Clark - Background
Theoretical Physicist (University of Cambridge)
1979-1992 research on atmospheric pollution problems in (then public) electricity industry.
  Acid rain
  Photochemical oxidants
  Modelling and field measurement (aircraft, ground-based) – collaboration with Met Office and various universities.
1992-2010 Met Office career largely focussed on small-scale and short-range forecasting:
  1993-1995 responsibility for improving operational UK mesoscale forecast model,
  1995-1998 Leader of Local Forecasting R&D Group responsible for developing ‘Site Specific Forecast Model’ (SSFM).
  1998-2008 Leader of Mesoscale Modelling group (JCMM, Reading) responsible for developing convective-scale non-hydrostatic model, especially forecasting thunderstorms and flash floods.
  2008-2010 Head of Joint Research Centres (JCMM at Reading University and JCHMR at CEH Wallingford).
Joined Surrey (Maths and Engineering) July 2010: Chair in Environmental Flow Modelling

## Slide 3: Outline
What is Colpex?
Some revision on atmospheric boundary-layer turbulence.
The Colpex experimental setup.
Modelling with the Unified Model
  Strategy
  Setup
  A case study.
Questions

## Slide 4: COLPEX Cold Air Pooling Experiment
  Formation of cold air pools in/near Clun Valley, Shropshire, England: small-scale, rolling terrain ~200 m valley-summit, ~1 km wide
  Field campaign: June 2009 – April 2010
  Collaboration between Met Office and Universities of Leeds and Surrey
  Intensive ground-based network combined with upper-air and remote sensing measurements
  Extensive modelling at very high resolution

## Slide 5: Terrain
Jeremy Price

## Slide 6: Acknowledgements
Met Office
  Cardington: Jeremy Price, Bernie Claxton, Volker Horlacher.
  Exeter: Simon Vosper, Adrian Lock, Peter Sheridan, Aurore Porson, Andy Brown.
  JCMM Reading: Emilie Carter, Humphrey Lean
Leeds
  Andrew Ross, Bradley Jemmett-Smith, Fay Davies
31st ICAM (International Conference on Alpine Meteorology), Aviemore, May 2011. (Esp. paper presented by Simon Vosper co-authored by many of the above including myself).

## Slide 7
Motivation and aims
Hazards - ice, fog
(Regional climate, pollution, crop exposure)
Small scale, difficult to forecast
Mechanisms/factors involved in cold pool formation at these scales (sheltering, drainage?)
How well does forecast model, running at very high resolution, simulate these cold pools?
Parametrization of surface exchange in larger scale models.
Temperature downscaling techniques in complex terrain

## Slide 8: Horizontally-Homogeneous (1D) steady state TKE budget
Reynolds Averaging
Shear Prod.
Bouyant Prod.
Transport
Dissipation
TKE production =
No production if sufficiently stable

## Slide 9: Eddy Diffusivity and Mixing Length Theory (Prandtl)
Transport~0
Assume:
So:
‘Equilibrium’ TKE given by:
No turbulence if sufficiently stable

## Slide 10: Surface Energy Budgets
‘Surface’ energy budget
H
E
G
LW_out
LW_in
SW_in
SW_out
H=Turbulent ‘sensible’ heat flux.
E=Turbulent ‘latent’ heat flux.
G=‘Ground’ heat flux
Surface
LW_out-LW_in+H+E-G=SW_in-SW_out
H+E-G=RN
or
At night, clear sky, light wind, surface temperature dominated by balance of radiative cooling and ground heat flux, with (perhaps) some turbulent flux to surface.

## Slide 11: Surface-layer similarity (Monin-Obukhov)
Three length scales: Ug/f (very large), z0 (very small), L:
Non-dimensional Shear
Non-dimensional Profiles
No solution if sufficiently stable

## Slide 12: Eddy Diffusivity and Mixing Length Theory
Thus
Unknowns:
CX (just a constant), mixing length (Blakadar formula) and ‘stability function’ f(Ri).
No equilibrium turbulence exists for Rf>1.
Kelvin-Helmholtz instability (etc.) leads to idea of critical Ri~0.25.
Ri
f(Ri)
0.25
0
1
These ‘simple’ parametrizations work well if surface heat flux or temperature specified.

## Slide 13: Stable Boundary Layer Parametrization in Real Climate and NWP models
Using ‘correct’ (local) stability functions in real models leads to problems, usually associated with excessive surface cooling and too great a tendency to ‘cut-off’ or ‘decouple’ the surface.
  Climate models may decouple much of extra-tropical winter land.
  An experiment in the ECMWF forecast model using ‘correct’ stability functions reduced skill by the equivalent of 10 years improvement!
  Even 1.5 km operational forecast model does not use ‘ideal’ function.
  Area-averaged fluxes from 1 km model over S England with ‘sharpest’ function do not follow this function.
Some stability functions used in the Met Office UM; only the ‘LEM’ function shows true critical Ri behaviour. Other functions retain vertical mixing far beyond that theoretically expected.

## Slide 14: ‘Real’ Stable Boundary Layers
H
E
G
LW_out
LW_in
Surface
Surface fluxes radiatively coupled to BL cooling as well as through turbulence.
H
E
G
LW_out
LW_in
Surface
And then there are slopes…

## Slide 15: Cold Pools
The ‘traditional’ view – drainage flows.
Problems:
Actually promotes downwards transport of warm air.
- What about ambient wind?
Sheltered
Brown and Vosper, 2008
U
H
Key parameter =

## Slide 16: Instrumentation
Main Cardington MRU masts:
  Detailed measurement of atmospheric variables at multiple heights (wind, temperature, pressure, moisture, turbulence)
  Radiative (LW and SW) and soil measurements (moisture, temperature and heat flux); component fluxes available to reconstruct full energy budget
  Data logged at 10 Hz, averaged up to 1, 5, 10 and 30 min
Network of ~20 Hobo temperature sensors; transect and along-valley coverage
~10 Leeds AWS instruments: atmospheric variables and ground temperature
Valley volume and profile measurements:
  1.5mm pulsed Doppler LIDAR (70x30m range gates), continuously operating
  IOPs: radiosondes hourly at mast locations; temperature survey car

## Slide 17
Instrument sites
3 main mast sites
Instrumented transects
Along-valley coverage
General sampling of the terrain
2 km

## Slide 18: Main mast sites
Springhill farm, 30m mast (exposed hilltop site)
Photos: Jeremy Price, Peter Clark
Duffryn (Clun valley)
50m mast
Burfield valley, 30m mast

## Slide 19: Intensive Observation Periods (IOPs)
Seventeen IOP nights:
View over Clun valley, 10/12/2009 (Jeremy Price)

## Slide 20: Snow and fog, January 2010
Jeremy Price

## Slide 21
Cold pool example – 9-10/9/2009
Strong inversion forms at Duffryn after sunset
Inversion shallow at Springhill
Negative peak of sensible heat flux after which temperatures relatively static at Duffryn
Overnight wind: Duffryn < 1 ms-1 Springhill ~ 3 ms-1
Temperature (°C)
Temperature (°C)
Sens. Ht. fx (Wm-2)
Sens. Ht. fx (Wm-2)
Mast temperature (°C) and sensible heat flux
0
25
0
20
-50
100
200
-100
surface screen 10m 25m 50m
midday
midday
midday
3pm

## Slide 22: Numerical modelling strategy
Test and optimise model configuration using IOP nights before running for entire winter period 2009-2010.
  Sensitivity studies examining the dependence of results on vertical resolution, time step, sub-grid mixing schemes, soil moisture content etc..
Simulation of the period as a whole to help:
  characterise the encountered cold pools generally
  elucidate, alongside observations, the dominant processes, parameters involved in cold pool formation
Extra simulations of IOPs, increasing resolution or adjusting parameterisations to examine cold pooling process in detail.

## Slide 23: IOP Case study Key Questions
How well can an operational forecast model simulate cold-air pooling on sub-kilometre scales?
Which physical processes (in the model) dominate the formation and evolution of cold air pools?
  Advection
  Sheltering (suppression of turbulent mixing aloft)
  Radiative cooling

## Slide 24: Model Configuration
Met Office Unified Model:
  Non-hydrostatic deep atmosphere fully compressible dynamical core
  Semi-implicit semi-Lagrangian dynamical (SISL) core
  Comprehensive parametrizations – sub-surface temperature and moisture, tiled surface-exchange, boundary-layer (see below), radiation (includes slope but not sheltering), clouds and 5 phase precipitation.
100 m (0.0009 degree rotated lat/long) horizontal resolution over 30 km square.
Variable resolution outside stretching (5.5%) to 1.5 km. (412x412 domain covering ~100 km square).
70/140 levels, 5 s timestep.
3D Smagorinsky, LEM stability functions, Cs=0.15.
RHcrit=0.99 in first 10 layers then gradual increase – 0.9 above level 30.

## Slide 25: COLPEX_100 Run Configuration
Operational UK 4 km:
Analysis (3D VAR+LHN) every 3 h
Output LBCs T+1 to T+4 every 15 min
‘HRTM’ 1.5 km:
Starting from reconfigured 4 km T+1 every 3 h.
LBCs every 10 min
COLPEX_100 run continuously:
Case study started from 16 UTC doubly reconfigured UK 4 km.
Own previous run thereafter.
Only impact of observations is through LBCs.

## Slide 26: COLPEX_100 Orography
Colpex_100
Domain
100 m inner
Domain
DTED ~100 m source data
Upper Dyffryn
Spring Hill
Burfield
D=1.5km
D=100m
Stretching zone
D=100m
Clun vallley
30 km
30 km

## Slide 27: Vertical grid and timestep
Operational grid: 70 levels up to 40 km
  5 q-levels below 112m
Enhanced resolution: 140 levels up to 40km
  12 q-levels below 112 m
100m model uses a 5 second timestep
  For 20 ms-1 winds aloft, this implies a horizontal Courant number of 1.
Made possible via SISL formulation of model

## Slide 28: 9th September 2009 IOP
© Crown copyright Met Office
Initial focus on the clear-sky COLPEX IOP
Simulation from 15UTC 09 to 15 UTC 13 September 2009
00 UTC 10/09/2009

## Slide 29: 20090909-10
70L
140L

## Slide 30: 20090909-10
140L
70L

## Slide 31: Potential temperature at 2m
2009/09/09 1800 UTC
2009/09/09 1900 UTC

## Slide 32: Potential temperature at 2m
2009/09/09 1800 UTC
2009/09/09 1900 UTC
2009/09/09 2000 UTC
2009/09/09 2100 UTC

## Slide 33: Potential temperature at 2m
2009/09/09 2200 UTC
2009/09/09 2300 UTC

## Slide 34
North-South section through Upper Dyffryn, Clun Valley
q (oC)

## Slide 35
q (oC)
Dx=1.5 km
Clearly 1.5km resolution is inadequate!
North-South section through Upper Dyffryn, Clun Valley

## Slide 36: Model screen temperature: D=100m L140 vs D=1.5km L70
© Crown copyright Met Office
Duffryn
Temperature minima well represented
Daytime temperatures too cold
Clear benefit of 100m resolution over 1.5km

## Slide 37
© Crown copyright Met Office
Duffryn (Clun valley) Springhill (hill-top) Burfield (valley)
T(oC)
T(oC)
T(oC)
Wind speed (ms-1)
Wind speed (ms-1)
Wind speed (ms-1)
5
0
8
8
0
0
140-level 100 m model results
-model
-obs
3
7
5
7
9
7

## Slide 38: Cold pool strength
© Crown copyright Met Office
Repeatable nighttime DT of approx. -4 K
100m L140 model gives good prediction of DT amplitude
Coarser vertical resolution (L70) results in weaker cold pools

## Slide 39: Heat budget
Q: What are the dominant sources of cooling?
Can use the model q budget to identify which are the important processes at different times during the night.

## Slide 40
Cooling in valley is relatively rapid around sunset.
Later on, hill-top and valley cooling rates are similar
Model heat budget suggests early rapid cooling in valley is largely due to greater turbulent heat flux divergence (relative to advection)
Model level 2 ~5m
(Advection and div.(heat flux) * 0.2)

## Slide 41: Conclusions
The model provides a credible simulation of clear-sky cold-pool cases observed during COLPEX
  Some room for improvement still.
  Foggy cases are more challenging!
The results show clear benefit of using enhanced vertical resolution. 100m horizontal resolution appears to be sufficient, but further refinement might be beneficial.
Results show some small sensitivity to stability functions used in turbulence parametrization scheme.

## Slide 42: Conclusions (contd)
Analysis of the model near-surface q evolution in and outside the valley suggests that:
In agreement with the observations, relatively rapid cooling occurs in the valley around sunset. Following this, the hill-top and valley cooling rates are similar.
This rapid valley cooling rate is largely due to large turbulent heat flux divergence. This is presumably due to:
  Strong surface cooling and reduced downward turbulent heat flux aloft, due to sheltering in the valley.

## Slide 43: Next?
‘Physics’ issues
  Turbulence scheme:
    Stability functions.
    Mixing lengths in shallow drainage flows.
    True horizontal mixing.
    Performance of TKE scheme.
  Surface exchange:
    Single tile at 100 m?
    Rivers and wet soil treatment.
    Land-use accuracy – esp. deciduous trees.
    Canopy impacts on drainage flows.
  Cloud scheme
    RhCrit
Dynamics settings
Long runs
  Statistical comparisons with observation data.
  Evolution of sub-surface.
  Downscaling.
  Parametrization.

## Slide 44
Thank you for Listening
Any questions?

## Slide 45: COLPEX: Example case study 14-15 October 2009

## Slide 46: Thank you for listening
Any Questions?

## Slide 47: Very Stable Valley Flows: COLPEX
Clun valley
Duffryn (Clun valley)
50m mast
Variable resolution MetUM 1.5 km -> 100 m
100 km
Met Office Site

## Slide 48: Very Stable Valley Flows: COLPEX
Clun valley
Duffryn (Clun valley)
50m mast
Variable resolution MetUM 1.5 km -> 100 m
100 km
Met Office Site

## Slide 49: 100 m resolution orography dataset 50 m resolution land-use dataset
D=1.5km
D=100m
Stretching zone
D=100m
Clun vallley
30 km
30 km
Upper Dyffryn
Spring Hill
Burfield

## Slide 50: Preliminary Results

## Slide 51: IOP model output
09-10 September 2009, potential temperature cross-section through Duffryn

## Slide 52: Observed and simulated cold pool, 09-10 September 2009
Mature cold pool, strong inversion
Broad agreement
Observed inversion more intense?
Screen temperature, 0500 UTC 10 Sept 2009

## Slide 53: Current status and future plans
Current
  Overview paper submitted to BAMS
  Optimisation of 100m resolution model
  Assessment of 4 km driving model forecast (cloud/radiation)
  “Climatology” of the observation period
Planned
  Run optimised model for full period
  Analysis of the full instrument and model datasets to identify controlling parameters
  Detailed study of cold pool formation in individual cases (IOPs)

## Slide 54: Synoptic influences - background
Form in presence of strong nocturnal radiative deficit
Inhibited by turbulent mixing (disturbs temperature gradients, drainage)
Aided by synoptically weak situations, terrain sheltering
Vosper & Brown (2008): flow coupling through gravity wave motion; in situ cooling, no drainage required
Seek straightforward rules to connect unresolved scales to resolved scales - downscaling development

## Slide 55: Summary
Dependence of cold pool intensity on background wind and radiative balance
Decoupling of valley atmosphere from large scale
Nocturnal averages, case studies
Future work

## Slide 56: Parameters
“Cold pool intensity”:
DT=TDuffryn - TSpringhill (mast screen temperatures)
Radiative deficit:
Flw = LWDN / LWUP (mast 2m radiative measurements)
Background wind:
U from UK 4km operational forecast, lowest 150m
Non-dimensional valley depth:
NH/U from UK 4km operational forecast, lowest 150m
Nocturnal averages

## Slide 57: Cold pool intensity, DT vs. U, Flw
Contrast increases with decreasing U, Flw
Sharp change in DT
Colour → DT

## Slide 58: Decoupling - Duffryn
log(NH/U) tightly correlated with U, Flw
Enough scatter to study independent effect of NH/U on DT?
Sharp change in DT is at NH/U > 0.4
Colour → log(NH/U)

## Slide 59: Decoupling - Duffryn
Observed DT diverges later than in model
NH/U for decoupling also larger?
Colour → Flw

## Slide 60: Decoupling – valley depth
Vosper and Brown (2008) vary valley depth for given ambient conditions
Clun (Duffryn) and Burfield valleys have different depths (and shapes!)
Look for decoupling at:
  Neither location
  Duffryn only
  Both Duffryn and Burfield
Dq
NH/U
Burfield
Duffryn (Clun)
Springhill
~150m
~90m
Hc

## Slide 61: Initial MetUM setup: COLPEX_100
100 m (0.0009 degree rotated lat/long) horizontal resolution over 30 km square.
Variable resolution outside stretching (5.5%) to 1.5 km. (412x412 domain covering ~100 km square).
70 levels, 5 s timestep (both might need improvement).
3D Smagorinsky, LEM stability functions, Cs-0.15. Dry static adjustment above level 30.
RHcrit=0.99 in first 10 layers then gradual increase – 0.9 above level 30.

## Slide 62: COLPEX_100 Land Use
Deciduous Trees
Coniferous Trees
C3 Grass
Shrubs
Urban
Lakes
Bare Soil
Source:
CEH
LCM1990
25 m
Landsat-based.

## Slide 63: Run configuration
Free run interior. New LBCs every 4 km analysis/short forecast.
1.5 km reference reconfigured from analysis every 3 h.
Why free run?
  Purpose of model is physics response to best larger scale forcing.
  Soil temperature / moisture free to evolve properly.
  No spin-up issues (risk with soil moisture – consider nudge).
Free run 1.5 km reference too?

## Slide 64: Example case study 14-15 October 2009

## Slide 65: Comparison with 1.5 km
Note – not synchronised